## Slide 1: Digital Signal Processing Spectral Estimation Techniques II
Prof. Aldebaro Klautau Federal University of Pará (UFPA)
www.lasse.ufpa.br & www.ppgee.ufpa.br

## Slide 2: Periodogram
Spectral Estimation Techniques
Frequency bin width:
MS spectrum unit is Watts
We want the density in watts per hertz
W
W/hz
hz
Periodogram definition
Since the periodogram does not learn parameters, it is a non-parametric estimator

## Slide 3: Welch: averages of periodograms
Spectral Estimation Techniques
One periodogram is one estimate/measurement of of a random process
Welch’s improves variance by averaging the power over shorter windows, sacrificing frequency resolution
One estimate
Multiple combined
estimates

## Slide 4
nperseg = 1024
Frequency bin width:
Spectral Estimation Techniques
4
nperseg = 128
nperseg = 256
nperseg = 512
nperseg = 1024

## Slide 5: Filtering white noise shapes the noise spectrum like the filter
Spectral Estimation Techniques
5
White noise
Colored noise

## Slide 6: Autoregressive (AR) Modeling
AR model is widely used in speech coding to mimic voice spectrum
Prediction filter
Spectral Estimation Techniques
6
White Noise
Colored noise
White Noise
Model assumption:
is all-poles
Find coefficients of FIR filter with that minimizes output energy
Collected signal
Optimum (Yule-Walker) yields white noise with power

## Slide 7
Not satisfying the assumptions of the AR model (system has zeros)
Satisfying the assumptions of the AR model
Spectral Estimation Techniques
7
Far fewer coefficients compared to Welch’s method
Poles cannot create zeros, so AR model performs poorly near notches

## Slide 8: Spectrogram
Spectral Estimation Techniques
8
Speech
Piano
Nonstationary processes have time-varying spectrum
Spectrograms take multiple windows but do not combine them like Welch’s method
Speech

## Slide 9: Thank you!
Prof. Aldebaro Klautau. Federal University of Pará (UFPA)
www.lasse.ufpa.br & www.ppgee.ufpa.br